SITE DEVELOPMENT PLAN REQUIREMENTS

All applications for development in the precinct will be required to submit a Site Development Plan (SDP) to the Council and the Parkview Residents Association with the exception of Residential 1 developments. The SDP must include the following:

# PROPOSED DEVELOPMENT

Site Area

Proposed Number of Units

FAR			: total floor area, floor area of each unit, floor area of outbuildings

Coverage		: % related to buildings and carports/garages

Building Lines		: to be indicated on all boundaries

Height Restrictions	: heights of all buildings (no basement is allowed to protrude above     the natural ground line)

Contours:	: existing and new, retaining walls and banks to be indicated

Sections	: through the site and adjacent stands indicating relationships of buildings to the existing natural ground line, finished ground line and adjacent buildings

Access	: from adjacent street and to all units

Parking	: all parking provision must be shown

Boundary Walls	: position, height and materials

Parking	: all parking bays must be indicated

## BUILDING AESTHETICS

Building Materials 	: to be compatible with the context

Colour Palette	: to be compatible with the context

Roofs	: to be compatible with context

Boundary Walls	: to be compatible with context

## PRIVACY

The privacy of the adjoining properties must be ensured, as well as, privacy between proposed units.

# LANDSCAPING AND TREES

All existing trees must be indicated on the drawings as retained or removed. A tree planting and landscaping plan must be submitted

ENVIRONMENTAL IMPACT ASSESSMENT (EIA)

EIAs should be requested for developments proposed on stands which fall within an environmental control area and on land which faces a public or private open space.

# SIGNAGE

All signage to be used on the site during and after construction must be indicated.

# LIGHTING

All external lighting and security lighting must be indicated on the drawings and should not interfere with the residential character of the area and the adjacent stands.

# STORMWATER MANAGEMENT

Stormwater management must be indicated. Hard and soft surfaces must be indicated and tabled as a % of total area.

# INFRASTRUCTURE CAPACITY

The capacity of the existing infrastructure and services must be established by the developer in relation to the nature of the development proposals.

# ENVIRONMENTAL HEALTH REQUIREMENTS

Developers will have to familiarise themselves with the requirements of the Environmental Health Department prior to the commencement of any works on the development site.